# DSP PAW Specifications and Requirements
## Development board
Supported boards:
NUCLEO-L476RG from STMicroelectronics

Firmware requirements (for new boards):
- ChibiOS support
- USB Device functionality
- 1 ADC input with 12-bit resolution and support for up to 96kHz sampling rate
- 2 DAC outputs with 12-bit resolution and support for up to 96kHz sampling rate
- Timer capable of producing 96kHz tick with divisions down to 8kHz
- 96kB or more of RAM

## DSP add-on board
## Pinout
3.3V output / 5V input (USB power) / GND / GND / ADC signal input / DAC signal output / ADC “Input 1” knob / ADC “Input 2” knob	Signal input Signal output Generator output	VDDA / GND / DAC generator output / ---------------------------------------------------------------------------------------------------------------------------------------------------------------------------- / USB data lines

## Electrical and functional specifications

	Min	Typical	Max	Units
Signal input	-2.0(1)		+2.0(1)	Volts
Signal/generator output	-2.0(1)		+2.0(1)	Volts
VDDA		2.048		Volts
USB input power	3.6	5.0	5.5	Volts

Sampling rate	8	32(2)	96	kHz
Sample buffer size	100	4,096(2)	4,096	count
ADC/DAC resolution		12		bits
Processing latency	1(3)	128(2)(3)	512(3)	milliseconds

Algorithm binary size			16,384	bytes
Algorithm stack size		13,000(4)	15,360(5)	bytes

(1) Exceeding this specification may cause damage to the microcontroller.
(2) Default setting after power-on or reset.
(3) Determined by sample buffer size divided by sampling rate.
(4) This much stack space is guaranteed to be available for the algorithm.
(5) Usable maximum is less than this due to firmware overhead. Exceeding the usable maximum
      will interrupt algorithm execution.